## Slide 1
An Optimized AMPM-based Prefetcher Coupled with Configurable Cache Line Sizing
Qi Jia, Maulik Bakulbhai Padia, Kashyap Amboju and Huiyang Zhou
Department of Electrical and Computer Engineering
North Carolina State University

## Slide 2: Presentation Outline
Access Map Pattern Matching (AMPM) Prefetcher
Problems with AMPM
  Cold zone
  Inaccurate states within zones
Proposed Optimizations
Configurable Block Sizing (CBS)
Two-Level Prefetching
Hardware Overhead
Experimental Results
Conclusion

## Slide 3: AMPM
・・・
0xAB04
0xAB03
0xAB05
0xAB06
0xABFF
Cache Line
・・・
0xAB02
Prefetch
Access 3
Access 1
0xAB01
0xAB00
0xAAFF
Access 2
Init/0
Access/2
Access
Access
Pre-
Fetch/1
Prefetch
Current access

## Slide 4: Problems with AMPM
Cold Zone
  No Pattern is detected before the zone bitmaps is evicted from the zone table
… … | 0 | 2 | 0 | 2 | 0 | … … | 0 | 2 | 2
0x480
0x4c0
0x500
0x580
0x540
0x9c0
0xa40
0xa00
Last Access before zone eviction
… … | 0 | 0 | 0 | 0 | 0 | … … | 0 | 0 | 0
No pattern detected

## Slide 5: Problems with AMPM Cont.
Inaccurate States in Zone
  The bits in zone bitmaps cannot reflect the actual states. (i.e. block evictions)
… … | 2 | 2 | 2 | 2 | 0 | … … | 2 | 1 | 1
0x480
0x4c0
0x500
0x580
0x540
0x9c0
0xa40
0xa00
Access
Bitmap indicate “Access”, but is evicted previously
Cannot prefetch since AMPM treat it as accessed and assumes it remain in cache.
Prefetch Chance Lost!!!
… … | 2 | 2 | 2 | “2” | 0 | … … | 2 | 1 | 1

## Slide 6: Proposed Optimizations
Common Offset Table (COT)
  Record the most frequent accessed
  offsets across different pages
  Update on every demand access
  Only init prefetch from COT when
  COT gets high accuracy
… … | 1 | 2 | 2 | 1 | 0 | … …
… … | 0 | 1 | 2 | 2 | 0 | … …
… … | 0 | 1 | 2 | 1 | 0 | … …
Pref | Counter | Offset | LRU
Access map page 1
Access map page 2
Common Offset Table
Notes: Threshold : 5

## Slide 7: Proposed Optimizations Cont.
Conflict Table
  Record how inaccurate the current information is
  Each entry in the table is corresponding to one page
  The entry counter will be increased when
  inaccuracy is detected.
  The entry counter will be reset when the page
  is evicted out
… … | 0 | 1 | 2 | 2 | 0 | … …
3
1
7
… …
4
Cache miss
update
Access map page
Conflict Table
3
1
8
… …
4
Notes: Threshold : 12

## Slide 8: Configurable Cache Line Sizing
A block size monitor is used to select the best block size used for LLC.
Block size selection algorithm (consider bandwidth and performance)
    Score = hit – A * (access – hit) * block_size
The selected blk size will be used to
guide the LLC prefetch.

## Slide 9: Two-Level Prefetching
Specific for DPC2 framework.
Change the state “Prefetch” in access map to “L2 Prefetch” and “LLC Prefetch”.
Our main goal is to hide long main memory latency. And then try to hide the LLC latency.
During prefetch candidate selection, we will first choose the blocks which are not prefetched. If the such candidates do not fill up the prefetch degree we will choose the blocks which are in “LLC prefetch” to transfer them into L2 cache.

## Slide 10: Hardware Overhead
Components |  |  | Storage
Memory Access Map Table | Address Tag (64 b) LRU (6 b) Access Map (3*64 b) | 64 entries | 2.047KB
CBS monitor | ATD | 4 ATD | 2.872KB
Common Offset Table | Counter (6 b) LRU status (6 bits) Offset Map(64*6 bits +64*1bit) | 8 entries | 0.45KB
Conflict Table | Counter (6 bits) | 64 entries | 0.046KB
Prefetch Bit | Prefetch (1 bit) | 4096 blks | 0.5KB
Cold Zone MSHR | Tags (64 bits) LRU status (5 bits) | 32 entries | 0.27KB
Total |  |  | 6.185KB

## Slide 11: Experimental Results
The optimized prefetcher outperforms the baseline without prefetching by 10.8%. Compared with the original AMPM, it achieves a speedup of 0.76% on average

## Slide 12: Conclusions
We optimize the AMPM prefetcher by introducing two hardware components: common offset table and conflict table.
We combine the AMPM prefetcher with configurable block sizing and two-level prefetching mechnisim.

## Slide 13: Question